## Slide 1: PAPER DELIVER BY THE CHAIRMAN OF ALTON, ENGR. GBENGA ADEBAYO AT THE NCC’S STAKEHOLDERS CONSULTATIVE FORUM FOR THE YEAR 2013 TO 2017 STRATEGIC MANAGEMENT PLAN HELD AT MUSON CENTRE ON FRIDAY 30TH MARCH, 2012

## Slide 2: TOPIC
“QUALITY OF SERVICE, TARIFF AND COVERAGE: ISSUES AND EXPECTATIONS”

## Slide 3
Energy & Power Issues: which necessitates two generating sets at each BTS site, which is compounded by frequent theft of the generators and diesel. The huge amount spent on diesel, generating sets and other associated expenses could otherwise be spent on network expansion in order to provide qualitative services to Nigerians.
Multiple Taxation and Regulation by myriad Ministries, Departments and Agencies of the Federal, State and Local Governments. The unpleasant intervention in basic operations by various Ministries Department and Agencies (MDAs) who issue stop work orders, seal, remove equipment and infrastructure in a bid to enforce their demands for payment of revenues and levies by service providers. Same infrastructure subjected to several regulatory oversight and fee demand

## Slide 4
Security Challenges & vulnerability of telecommunications infrastructure (theft, vandalisation and sabotage of network equipment, etc) impede our capacity to carry out timely equipment upgrades, thereby impacting negatively on QoS. We also note that our operations are not immune from the intermittent community issues and civic unrest in various regions, which also often result in denial of access, illegal detention of site personnel, vandalisation of installations, etc., contributing to protracted site deployment timelines. Road construction and other unplanned civic works often result in damage to site installations.
  Environmental & Community Issues: agitation and militancy across the six geopolitical zones (especially Lagos, Niger Delta, South East) restricts rollout, constraints maintenance & refueling of sites. The number of BTS sites locked out or inaccessible are increasing by the day on account of Community issues.

## Slide 5
Infrastructure: Limited incumbent interconnectivity & transmission infrastructure: NITEL suppose to be the backbone infrastructure for Service Providers to ride upon
  Increasing burden of developing national transmission capacity on Operators
  Epileptic power supply from National Grid - additional cost of self generation of power
  Immature supporting local manufacturing industry, therefore reliance on imports & time consuming custom processes e.g. 3 weeks to clear consignments, 2 weeks average lead-time to process shipments
  Limited rail & road transport infrastructure & integrated distribution networks

## Slide 6
  These challenges seriously affect our ability to deliver the desired Grade of Service across the Federation. Whilst the industry continues to device strategies for dealing with these issues, the concerted effort of all stakeholders is required to protect the industry and assure its sustainability.

## Slide 7
COVERAGE
As background, it should be noted that Sites are generally planned to enhance capacity and coverage. From planning to deployment, there several processes which seek to ensure that sites are built to deliver qualitative services to esteemed Nigerian subscribers. These include the following:
Radio Frequency (RF) Planning Site Survey /Site Release: Consideration is given to the capacity /coverage requirements of the network. The process is designed to ensure that all Quality of Service expectations are met.
Transmission Planning Line of Site Survey: This seeks to ensure contiguous transmission and connection of new site to the rest of the network, including adjacent sites.
Site Acquisition Process: This involves negotiation with landlords of plots on identified locations.
Stakeholders Technical Site Survey (TSS): Once the property for site is acquired, a technical site survey is conducted to confirm suitability of the site for network operations.

## Slide 8
Planning for sites in high-capacity areas involves extensive planning to optimize network performance with regard to extent of coverage and quality of network performance. Due to subjective considerations imposed by population density in the built up urban areas, there are however certain key considerations which must be considered to ensure that QoS is addressed. These are as follows:
1. Capacity Planning/Metropolitan Expansion
Capacity sites are planned to increase and/or improve network capacity in areas where the need is required.
In planning such sites, it is important to consider the following:
  The impact of the site on other adjacent sites in the area from a frequency planning perspective.
  The positioning of the site with respect to the amount of traffic that it will generate from adjacent cells, in the same coverage area
  The impact that the site will have on future network expansion, which is linked to traffic expansion and coverage requirement

## Slide 9
In urban areas, it is important to use buildings to both direct and contain the signal. Masts that are in use should be no higher than 35m in urban areas to provide a basis for expansion of a mini-cellular network, and stub masts on building rooftops are used as much as possible subject to availability.
Sites should be developed as part of a larger plan rather than planned individually with congestion relief sites built to relieve congestion on existing cells where required.
2. Dominant Server Coverage
There is a need for dominant servers to be planned in areas where interference is high due to the coincidence of several signals of a similar level (all occupying the same frequency). These signals may be of a high or low level.
As this generally occurs in areas of high visibility such as hilltops, high buildings and ridges, it is important to contain the coverage of this type of site to the problem area itself.
It is important not to create problems elsewhere in the network while solving a local interference problem. This we can only achieve by proper positioning of new sites.

## Slide 10
3. Coverage Consolidation Sites
Low coverage consolidation sites are required in areas where the signal is below acceptable levels for in-building coverage. These sites are typically in urban areas and in business parks where in-building coverage is required throughout the building/s concerned. The closer the site the better the indoor coverage of buildings around it. In urban areas where in-building coverage is to be consolidated, it is important that buildings be used to form a natural barrier. The use of microcells of small specified areas is encouraged.
In suburban areas, it is essential that environmental concerns be addressed to blend sites into the surrounds. It is particularly important that these sites be positioned according to a nominal grid plan and that they are targeted at a particular problem area rather than attempting to maximize coverage. The effect on trees, rocks, buildings and vegetation are taken into account.

## Slide 11
Samples of the estimated processing times for permitting and approvals encountered across the regions have been distilled into the tables which appear below.
RIGHT OF WAY AND SITE BUILD PERMIT MATRIX
TABLE 1.0 - Right of Way (RoW) Approval Process for Federal Ministry of Works
Responsibility
Task
Timelines
Network Operator
Application for Right of Way is sent to the Federal Ministry of Works
1 Day
Federal Ministry of Works
Responds with a demand notice
3 – 8 weeks
Network Operator
Process payment according to demand notice
1 week
Timeframe for securing Right of Way from Federal Ministry of Works is an average of 8 weeks
TABLE 1.1 - RoW Approval Process for Lagos State
Responsibility
Task
Timelines
Network Operator
Network Operator sends request to State government on intention to acquire right of way on selected streets.
1 Day
State Government
State Government receives request, confirms streets and releases demand notice to Network operator.
3 - 18 Weeks
Network Operator
Network operator process demand notice and effects payment.
2 Weeks
Timeframe for securing Lagos RoW is an average of 20 weeks

## Slide 12
TABLE 1.2 – RoW Approval Process for a Sample of Other States
TABLE 2.0 – Site-Build Permitting Process
Region
Northern states including FCT ABUJA
Comments
Duration
4 - 12 weeks
Insistence on engaging nominated agents for the EIA outside the Federal Ministry of Environment framework. FCT approvals are usually not issued in good time. Niger State asks for as high as N950,000.
Amount
Average of N350,000.00
Additional Demand for a local EIA from FCTA
100,000.00
Mobilisation
Allowed after payment is receipted
Region
Eastern States
Comments
Duration
2 - 4 weeks in some states its uncertain
Varies from State to State. The major challenge here is the insistence on engaging nominated agents for the EIA outside the Federal Ministry of Environment framework and the inclusion of additional payments (Sanitation Fees). Delta state requests for payment of N650,000.00 and Cross River States Govt is presently requesting for N1.5m
Amount
Fees from 350,000.00 to N1.5 million per site
EIA
25,000.00
Mobilisation
Only after approved drawing is released by state planning authority
Region
Western States
Comments
Duration
3 - 8 weeks
Varies from State to State. The major challenge here is the insistence on engaging nominated agents for an additional local EIA outside the Federal Ministry of Environment framework, and also the inclusion of additional charges (Site Analysis Report) in Oyo State. Og un State N500, 000.00, Oyo State N350, 000. 00.
Amount
Average of 500,000.00
Additional Demand for local EIA
Ranges around 150,000.00
Mobilisation
After payment
Mobilisation
After payment
In most cases, operators are operators are faced with an uncertain approval framework which leaves operators at the whims and caprices of the approving authority and its officers. Attached as annexure 2 is a process flow chart which illustrates the process involved in rolling out telecommunications infrastructure.